## Slide 1: ACL – Solution for Assignment 1
West(config)# access-list 111 deny ip 10.10.1.0 0.0.0.255 10.10.4.0 0.0.0.255
West(config)# access-list 111 permit ip 10.10.1.0 0.0.0.255 10.10.0.0 0.0.255.255
West(config)# access-list 111 permit tcp 10.10.1.0 0.0.0.255 any eq 80
West(config)# access-list 111 deny ip 10.10.1.0 0.0.0.255 any
West(config)# access-list 111 permit ip any any
West(config)# interface f0/0
West(config-if)# ip access-group 111 in
=> qui tắc là permit trước rồi chặn sau
=> thứ tự rất quan trọng
=>sau khi viết xong ACL phải add vô 1 cổng gần LAN1 nhất -> interface f0/0
=> lưu lượng đi vào -> ip access-group 111 in
10.10.0.0/16 - mượn 8 bit -> 10.10.z.0/24
10.10.2.0 2=00000010
10.10.3.0 3=00000011
-------------- ---------------
0.0.?.255 00000001 = 1
=> WILDCARD: 0.0.1.255
Thay vì dòng 2 ghi 10.10.0.0 0.0.255.255
(10.10.0.0/16 như là cha của 10.10.2.0 & 10.10.3.0/24)
thì có thể ghi: 10.10.2.0 0.0.1.255

## Slide 2: ACL – Solution for Assignment 2
West(config)# ip access-list extended ONE_AND_TWO_WAY
West(config-ext-nacl)#permit tcp 10.10.2.0 0.0.0.255 10.10.4.0 0.0.0.255 eq 21
West(config-ext-nacl)#permit tcp 10.10.2.0 0.0.0.255 10.10.4.0 0.0.0.255 gt 1023
West(config-ext-nacl)#deny ip 10.10.2.0 0.0.0.255 10.10.4.0 0.0.0.255
West(config-ext-nacl)#permit tcp 10.10.2.0 0.0.0.255 10.10.3.0 0.0.0.255 eq 80
West(config-ext-nacl)#permit tcp 10.10.2.0 0.0.0.255 eq 80 10.10.3.0 0.0.0.255
West(config-ext-nacl)#deny ip 10.10.2.0 0.0.0.255 10.10.3.0 0.0.0.255
West(config-ext-nacl)#permit ip any any
West(config-ext-nacl)#exit
West(config)# interface f0/1
West(config-if)# ip access-group ONE_AND_TWO_WAY in

## Slide 3: ACL – Solution for Assignment 3
Gateway(config)# ip access-list extended GATEWAY
Gateway (config-ext-nacl)# deny icmp any any echo
Gateway (config-ext-nacl)# permit tcp any 10.10.1.2 0.0.3.0 eq 80
Gateway (config-ext-nacl)# permit tcp any any established => cho phép từ trong ra ngoài
Gateway (config-ext-nacl)# deny tcp any any
Gateway (config-ext-nacl)# permit ip any any
Gateway (config-ext-nacl)# exit
Gateway (config)# interface f0/0
Gateway (config)# ip access-group GATEWAY in

## Slide 4: ACL – Solution for Assignment 4
Extended IP access list GATEWAY
ip access-list extended GATEWAY
10 deny icmp any any echo => internet không ping vào trong network được
30 permit tcp any any established
40 deny tcp any any
50 permit ip any any

## Slide 5: ACL – Solution for Assignment 5
Extended IP access list WEST =>
ip access-list extended WEST
deny ip 10.10.1.0 0.0.0.255 10.10.2.0 0.0.0.255
deny ip 10.10.1.0 0.0.0.255 10.10.3.0 0.0.0.255
permit ip 10.10.1.0 0.0.0.255 10.10.4.0 0.0.0.255
permit tcp 10.10.1.0 0.0.0.255 any eq 80
deny ip 10.10.1.0 0.0.0.255 any
permit ip any any
interface f0/0
ip access-group WEST in
end
write memory

## Slide 6: ACL – Solution for Assignment 6
ip access-list extended WEST
permit tcp 10.10.2.0 0.0.0.255 10.10.3.0 0.0.0.255 eq 21
permit tcp 10.10.2.0 0.0.0.255 10.10.3.0 0.0.0.255 gt 1023
deny ip 10.10.2.0 0.0.0.255 10.10.3.0 0.0.0.255
permit ip any any
interface f0/1
ip access-group WEST in
end
write memory
ip access-list extended EAST
permit tcp 10.10.3.0 0.0.0.255 10.10.2.0 0.0.0.255 eq 21
permit tcp 10.10.3.0 0.0.0.255 10.10.2.0 0.0.0.255 gt 1023
deny ip 10.10.3.0 0.0.0.255 10.10.2.0 0.0.0.255
permit ip any any
interface f0/0
ip access-group EAST in
end
write memory
ftp ip...
dir
get <copy 1 đoạn tên file bỏ dô>
quit
dir